# ELEC ENG – ECE756 Design of Lightwave Communication Systems and Networks

# INSTRUCTOR NAME

# S. Kumar

DURATION OF EXAMINATION: 3 hours                                                  April 16, 2009

McMASTER UNIVERSITY FINAL EXAMINATION

THIS EXAMINATION PAPER INCLUDES 5 PAGES AND 6 QUESTIONS. YOU ARE RESPONSIBLE FOR ENSURING THAT YOUR COPY OF THE PAPER IS COMPLETE. BRING ANY DISCREPANCY TO THE ATTENTION OF YOUR INVIGILATOR.

Special Instructions:

Use of any calculator is allowed.

Answer all the questions.

# Good luck and have a great summer!

- Electrical field intensity in a medium is given by the three dimensional wave equation

Show that its solution is

,

where f is an arbitrary function and

4 marks

2a. The average optical power output of the transmitter shown in the figure is 2 mW.  The fiber-optic link consists of a transmission fiber (TF) followed by a dispersion compensation fiber (DCF). The transmission fiber has a dispersion coefficient (β2 ) = -21 ps2 /km, loss coefficient = 0.25 dB/km and length = 50 Km. The DCF has a loss coefficient of 0.3 dB/km. The output of the DCF is connected to an amplifier of gain G= 18 dB. (a) Find the length of DCF so that the average output power of the amplifier is 3 mW. (b) Find the dispersion coefficient (β2 ) of the DCF such that the pulse width (FWHM) at the output of DCF is twice the pulse width (FWHM) at the input of the TF. Assume that a Gaussian pulse with FWHM = 12.5 ps is incident on the TF. Ignore β1 .

7 marks

(Hint: Suppose a Gaussian pulse with half-width at 1/e-intensity point T0 is incident on a fiber system with the transfer function

,

electric field envelope at the output is given by

2b. Explain the meaning of (a) numerical aperture and (b) Rayleigh scattering in optical fibers.                                                                                                              4 marks

3a. A 250 micron long InGaAsP  laser has an internal loss =  40 cm-1 , mirror loss =

100 cm-1, refractive index = 3.4. Calculate (a) photon life time and (b) threshold

electron density. Assume that gain varies as G = G0(N-N0) with G0 = 2.64 x 10-12

m3/s    and N0 =  0.5 x 1024 m-3.                                                                   5  marks

3b. In a direct band-gap material, an electron in the conduction band having a crystal momentum of 7.84  Kgm/s makes a transition to the valence band emitting electromagnetic wave of wavelength 0.8 micron. Calculate the band-gap energy.  Assume that the effective mass of electron in the conduction band is 0.07m and that in the valence band is 0.5m where m is the electron rest mass. Assume parabolic conduction and valence bands.                                                                                                   5 marks

4a. A photodiode has the following parameters:

Time constant of RC circuit (τRC) = 0.5 ps

Drift speed vd = 105 m/s

Absorption coefficient α = 2 x 106 m-1.

This photodiode is used in a receiver circuit of an optical transmission system operating at 10 Gb/s. It is desired that the bandwidth should be > 10 GHz and quantum efficiency η > 0.8. Find the range for depletion layer width w that satisfies the above design constraints.                                                                                                         5 marks

4b. Show that the SNR of a PIN photo-detector in the presence of shot noise and thermal noise is given by

where  is the responsivity,  is the incident power, =effective bandwidth  , =load resistance, = absolute temperature.                                                5 marks

5a. Two amplifiers with gain G1 and G2 are connected in tandem as shown in the figure. Derive a mathematical expression for the variance of the noise current due to signal-amplifier noise beating.  Assume that the spontaneous emission factor nsp is unity for both amplifiers and the power spectral density of the amplifier j is

where  =Planck’s constant, f = optical frequency. Assume that is one-sided

bandwidth of a receiver (assumed to be ideal low pass filter) and  is the transmitter output power.                                                                                                  5 marks

# 5b. Explain the difference between direct detection and coherent detection schemes. Can you detect the PSK signal using a coherent detector?                                           4 marks

6. The input power of a MZ modulator is P. It is desired that the output power of a MZM is P for bit ‘1’ and P/2 for bit ‘0’. The message signal, m(t) to the MZ modulator is a polar NRZ with A volts for bit ‘1’ and –A volts for bit ‘0’.  If the half-wave voltage, = 3 V, find A and the bias voltage. Assume that the MZ modulator is lossless and chirp-free. Choose A and bias voltage such that their absolute values are the lowest (for minimum power).                                                                                               6 marks

# Useful information

Speed of light in vacuum          c                        2.99793m/s

Electron charge                         q                        1.60218 C

Electron rest mass                     m                        9.109  Kg

Planck’s constant                      h                         6.625J.s

Boltzmann’s constant               kB                        1.38054J/K

1 eV = 1.60218 J.

# The power in dBm unit is given by

# Numerical Aperture, NA =

=core index, and = cladding index.

# The transfer function of a single mode optical fiber is given by

# For Gaussian pulse

=half width at 1/e-intensity point.

The quantum efficiency η and responsivity R of a photodiode are related by

# The power spectral density (PSD) of shot noise is

# and that of thermal noise is

# Total loss in the cavity is given by

# Photon life time is

v is velocity of light in the medium.

# The rate equations governing photon density and electron density are given by

# The threshold current density is

# Optical power generated in a semiconductor laser is

# Energy density = photon density * h*f

# Optical intensity = energy density * v

# MZ modulator transfer function:

# THE END

# Text boxes

Tx               TF        DCF         Amp                  Rx  Rx

G2

G1

Tx                   Amp1          Amp2              Rx